## Slide 1: Cheaper doesn't mean better
Cheap is fine, blind risk-taking is not
Marco Paesani | #EPF2026 | September 14 - 16th, 2026

## Slide 2: Meet the Speaker
Infrastructure & Core Network Specialist (Civil & Military Systems)
Dedicated to improving network performance and security
IPv6 & SRv6 Visionary Engineer
Passionate about technology advancement and service reliability.
Network Architect at Warian AS56911
Marco Paesani | #EPF2026 | September 14 - 16th, 2026

## Slide 3: This talk is about the multiplier, not the price tag
Big IX is where you deliver over 50% of your CDN's real-time traffic where and your optical interconnect fails (transceiver and/or patch).
One or two RS on IX are not responsive to topology changes or BGP redesigns, and you deliver traffic to who knows whose IP address.
After a core link fails, your software router with OSPF, LDP, BGP, and MPLS cannot coordinate traffic, even with correct advertisements to a peering LAN.
Do you have any other experiences with this type of problem?

## Slide 4: Executive Summary
The Premise: In Internet Service Provider (ISP) networks, cutting core infrastructure costs can trigger catastrophic compounding failures.
The Illusion: Low-cost transceivers, fibre, and routing hardware appear to save upfront Capital Expenditure (CapEx).
The Human Factor: Underfunded infrastructure overburdens engineers, driving away top technical talent.
The IXP Impact: Cheap hardware degrades peering relationships at Internet Exchange Points, threatening global connectivity.
The Reality: Extreme Operational Expenditure (OpEx), SLA penalties, and customer churn far outweigh and initial savings.

## Slide 5: 1. The Anatomy of a Cheap ISP Backbone
Optical Layer Shortcuts
Poorly tested: Using third-party transceivers that lack rigorous acceptance testing or DOM monitoring.
Low-Grade Fiber Paths: Leasing cheaper, poorly maintained dark fibre, prone to micro-bends.
Vulnerability: Micro-bends and low-grade optics lead to signal degradation and frequent flapping links.
Budget Routing Hardware
Small Buffers: Microbursts quickly become packet loss
Limited FIB/TCAM Headroom: Route growth and churn can slow or break convergence

## Slide 6: 2. IXP Risks: Damaging the Ecosystem
Route Server Flapping
The Threat: Underpowered routers cannot process rapid BGP updates at large public IXPs.
The Consequence: Your router drops sessions, causing data plane loops and black-holes for international traffic.
The Penalty: IXP operators may quarantine or disconnect your port to protect other members from stability issues.
Poor Port Management
Under-provisioning: Low-capacity IXP ports lead to severe packet drops during peak traffic hours.
Lack of Redundancy: Relying on a single IXP connection means a local switch failure cuts off your direct path to major Content Delivery Networks (CDNs) and cloud providers.
Financial Penalty: Forcing data over expensive IP Transit links instead of free IXP peering spikes operational costs.

## Slide 7: 3. Cheap networks pay engineers instead of vendors
The "Firefighting" Culture
Constant Crises: Engineers spend 100% of their time fixing cheap, broken hardware instead of optimising the network.
Burnout: Midnight emergency calls and 24/7 stress lead to high employee turnover.
Skill Gaps: Junior staff are often left to manage complex, unstable environments without proper training.
Brain Drain
Losing Experts: Top-tier Network Architects leave for companies with modern, reliable infrastructure.
Expensive Hiring: Replacing an experienced engineer involves high recruitment and onboarding costs.
Institutional Memory: When key personnel quit, critical network understanding and historical knowledge disappear.

## Slide 8: 4. Hidden Financial Destruction (The Real TCO)
Service Level Agreement (SLA) Penalties
The Contract: Enterprises demand 99.999% uptime ("five nines").
The cost: Just one hour of backbone network downtime can result in large automatic refunds for enterprise customers.
Exponential OpEx
Emergency Maintenance: Dispatching technicians for midnight fibre repairs costs up to 5x more than standard deployments (in our experience)
Truck Rolls: Frequent hardware replacements eat up field engineering hours.

## Slide 9: 5. Technical Consequences of Cutting Corners
Feature | Premium Backbone Hardware | Budget Backbone Hardware
BGP Routing Capacity | Full global routing tables with room to grow | Limited tables; prone to memory exhaustion
IXP Peering Capability | Smooth, high-throughput peering with multi-gigabit buffers | High packet drop rates during IXP micro-bursts
Personnel Workload | Automated monitoring; low maintenance | Constant manual troubleshooting and reboots
Vendor Support | 24/7/365 engineering escalation (TAC) | Delayed email support or self-service forums

## Slide 10: 6. The Domino Effect on Brand & Business
Cascading Customer Churn
Wholesale Loss: Downstream smaller ISPs lease capacity from you; if you fail, they leave permanently.
Consumer Frustration: Frequent packet drops destroy real-time traffic like gaming, VoIP, and video streaming.
Regulatory & Reputation Damage
Fines: Telecommunication regulators fine ISPs that fail to maintain critical infrastructure stability.
Reputation: Brand damage from a highly publicised backbone outage takes years to repair.

## Slide 11: 7. Strategic Investment Framework
Prioritise Resiliency over Low Cost: Implement dual-homed, geometrically diverse fiber paths.
Invest in Your Team: Provide vendor certification training to retain high-performing engineering personnel.
Optimize IXP Strategy: Deploy enterprise-grade edge routers with large buffers at IXPs to maintain peering reputation.
Automate Failover: Invest in advanced MPLS/SRv6 Traffic Engineering to reduce manual workloads during breaks.
Plan for minimum 5 Years: Size your core routers for future traffic scaling, not just today's capacity requirements.

## Slide 12: Our engineering rules and suggestion
Improve the skills and number of network engineers to professionally and accurately address SLA and customer expectations
Goods and services must exceed the target for a minimum of 5 years and must be valued for ROI and TCO with adjusted costs related to system failures
The primary cost remains time: find how to reduce effort without reducing service quality
All these points arise from my personal experience for over 40 years in the world of telecommunications, Internet specifically and this is a must on our network !

## Slide 13
The Network doesn't care what you paid. It cares how you fail ...
“ Unless you can name the last time your edge failed a BGP update burst, You are the risk to your IXP community ”

## Slide 14: Thank You !
Marco Paesani
mpaesani@warian.net